## Slide 1: Examples of Specific Laser Systems
Gas Lasers
  CO2 (9-10 m), High Power
  He:Ne (632 nm) , Ar (ion) Laser (520 nm)
  Excimer (UV) Lithography
Solid-State Lasers
Nd:YAG , Ti:Sapphire (Ultrafast Revolution)
Fiber Lasers (Rare-Earth Doped Fiber Lasers)
Yb3+ (10+ kW), Tm3+ , Ho3+ (2 m), Er3+ (1.5 m)
Dye Lasers
Chemical Lasers
COIL (7+kW), MIRACL (>1 MW !!)
Semiconductor Lasers

## Slide 2: Laser Market and Applications

## Slide 3
wavelength
100 nm
1 mm
10 mm
500 nm
Ultraviolet
Visible
Infrared
dye lasers
semiconductor lasers
excimer
lasers
solid-state lasers
molecular gas lasers
atomic gas lasers

## Slide 4
Proprietary Data
University of New Mexico
A
B
A
B
A
B
electronic transitions
vibrational transitions
rotational transitions
emission
VIS, UV
NIR, IR
FIR
Optical Transitions
1
2
1
2
discrete levels
energy bands
OR

## Slide 5
Proprietary Data
University of New Mexico
Typical laser efficiencies  :
Argon - ion < 0.1%
CO2 laser < 20%
Excimer < 20%
GaAlAs (diode laser) < 40%
HeNe < 0.1%
Nd:YAG < 10%

## Slide 6
Gas Lasers (Examples: HeNe, Ar+, Excimer, CO2,..)
The excitation mechanism in most gas lasers is via electric discharge

## Slide 7
The first Gas Laser: He-Ne
Ali Javan, et al. (Bell Labs, 1962)
The second working LASER system to be demonstrated.
The first gas LASER to be produced.
The first LASER to produce a continuous output beam
The active laser medium is a gaseous mixture of He & Ne atoms, in a roughly 10:1 proportion
The gas is enclosed in a cylindrical quartz DISCHARGE tube

## Slide 8
Laser Type
Linear Power Density
W/m
Maximum Power W
Power Efficiency
%
He-Ne
0.1
1
0.1
Argon
1-10
50
0.1
CO2
60-80
>104
15-20
Comparison of Gas Lasers

## Slide 9
C. K. N. Patel, "Continuous-Wave Laser Action on Vibrational Rotational Transitions of CO2," Physics Review, Vol. 136 A, (Nov., 1964) P. 1187
CO2 Lasers (9-11 micron)
Applications (pealing peanuts to star wars)
Industrial (cutting, welding, material processing)
Military (range finding, targeting, remote sensing, sensor blinding, destroying …)
Medical (cutting, skin resurfacing)
…..

## Slide 10
Transitions are between molecular vibrational-rotational levels.
C
O
O
Modes of vibrations:
Symmetric stretch
Asymmetric stretch
Bending mode
Molecular Vibrations and Rotations

## Slide 11
Simple Harmonic Oscillator (Quantum Mechanics):
C
O
O
C
O
O
C
O
O
(000)
(001)
(020)
(010)
(200)
(100)
10.6 m
9.6 m
J=50
…..
J=18
….
J=1
Rotational states
Symmetric Stretch
Bending
Asymmetric Stretch

## Slide 12

(m)
P- branch
JJ-1
P(50)
P(20)
001 100
001 020
10.4
10.6
9.4
R- branch
J J+1
P- branch
J J-1
R- branch
J J+1
R(17)
P(19)
CO2 Laser Transitions
Tuning:
diffraction grating
=9-11(m)

## Slide 13
Effect of Gas Mixtures: CO2+N2+He
(200)
(100)
(1)
(0)
Metastable
discharge excitation
(200)
(100)
He
N2
Nitrogen helps populating the upper laser level in a discharge
Helium helps to depopulate the lower laser level by collisions
Typical Mixture CO2/N2/He (1/3/5),….
Other possible additions to the gas mixture: CO, H2

## Slide 14
11.3 Gas Discharge Phenomena
+H.V.
e-
e+
Electrons emitted from cathode get accelerated by the electric field
The energetic electrons excite the vibrational modes of the gas molecule via inelastic collisions
cathode
anode
Example:
L=1 meter and P=25 torr
Need V=25 kV for optimum operation

## Slide 15
11.4 Specific Types of CO2 Lasers
High Power CW Operation
DC-Discharge
Longitudinal discharge (High Voltage: 10-100 kV)
Pressure: 10-100 torr
Multistage discharge tubes can be used to produce kilowatts of output power
RF-Discharge
In practice waveguides are used.
High discharge stability, high pulsing frequency (up to 100 kHz)
Expensive RF generator and requires EMI shielding
0.2 W/cm in a waveguide laser

## Slide 16
Laser Hardened Materials Evaluation Laboratory (LHMEL)
WP-AFB, Dayton, OHIO
Electric Discharge Coaxial Laser (EDCL)

## Slide 17
Gas-Dynamic Lasers
Basov & Oraevskii (1963)
Principle: Population inversion by rapid expansion (supersonic flow) of a super-heated gas
CO2+N2+H2
T=1000-3000 K
P=1-20 atm.
Inversion region
v= 105 cm/sec.
cw powers up to 1 MW have been obtained from gas-dynamic CO2 lasers !!

## Slide 18
HELEX
Gas-Dynamic Lasers
Large scale 135 Kilowatt gasdynamic laser at Avco Everett Research Lab.
High Energy Laser Experimental
Germany, 1970’s
C2N2 or CO

## Slide 19
Pulsed CO2 Lasers
Most Common: Transversely Excited Atmospheric (TEA) CO2 Lasers
CO2:N2:He
Pulsed H..V
Flowing or sealed systems
Pulsewidths from 50 ns to 300 ns
Repetition rates: 1Hz. to 1 kHz.
Pulse energy: 50 mJ to 10 J (amplified)
Low pressure gain cell
(for single longitudinal operation)

## Slide 20
Proprietary Data
University of New Mexico
Excimer (Exciplex) Lasers
Molecules exist only in the excited state
(Excimer=Excited-Dimer) or (Exciplex= Exciated-Complex)
XeCl* 308 nm
KrF* 248 nm
ArF* 193 nm
F2* 156 nm
A
B
excitation
A
B*
A
B
emission
of a photon
Applications: lithography, micromachining and eye surgery
Nikolai Basov*, V. A. Danilychev and Yu. M. Popov, at the Lebedev Physical Institute
Pulsed, Typically 10-50 ns, 5-20 mJ
*Nobel Prize, Physics (1964), Shared with Townes and Prokhorov

## Slide 21
Excimer Lasers
Eye surgery
Lithography

## Slide 22
Argon Ion Laser
488 and 514 nm
Ar+

## Slide 23
Organic Dye Lasers
Example: Rhodamine 6G

## Slide 24
Solid-State Lasers
(a) Nd3+ :YAG  = 1.064 m, 1.331 m
(b) Nd3+ :glass  = 1.062 m (silicate glass),  = 1.080 m (fused silica)
Hm3+ :YAG, Tm3+ :YAG  = 2.1 m
Yb3+ : YAG,  = 1.03-1.05 m
Ti3+ :sapphire,  = 0.7 - 1.1 m
Fe2+ :ZnSe  = 3.7 – 5.5 m
dopant
host crystal
The lasing atoms (ions) are fixed in a solid (crystal, glass).
Solid-state lasers can operate in continuous (cw) or various pulsed modes.
The active ions are most commonly either a rare-earth or transition metal elements
Examples:

## Slide 25
Optical Science & Engineering
University of New Mexico
The 4f-4f transitions in Rare-Earths Ions:
5S
6S
4f
Yb (Xe)4f136s2
Yb3+ = (Xe)4f12
Degeneracy:

## Slide 26
Rare-Earth Ion Doped Lasers
Lanthanides
Quasi Four-Level Lasers

## Slide 27
Maiman’s Ruby Laser

## Slide 28
Example: Nd:YAG laser
Energy diagram of Nd3+:
Output (Nd:YAG, Nd:YLF, Nd: YVO4 )
cw:  1000 W
pulsed: pulse energy  1 Joule
Q-switched – 5-20 ns pulse duration
modelocked – 10-100 ps pulse duration
YAG: Yttrium Aluminum Garnet (Y3Al5O12)
Nd replaces Y

## Slide 29
DPSS : Diode-Pumped Solid-State Laser
Similar to one used in our Optics Lab

## Slide 30
Diode Lasers for Pumping
High Power (Diode Bar) Fiber Coupled
Efficient (current injection)
High power
Designer Wavelength
Poor Beam Quality
Broadband (3-5 nm)
Semiconductor lasers will be covered in more detail (next lecture)

## Slide 31
DPSS : Diode-Pumped Solid-State Laser
From laser pointers (5-10 mW) to 100W lasers
Example Nd:YVO4 (Vanadate)
5-10mW
$20
5-10W
$10k-$40k

## Slide 32
Titanium doped sapphire (Ti3+ :Al2O3) laser
The jewel of ultrafast lasers

## Slide 33
Nobel Prizes
John L. Hall and Theodor W. Hänsch“
“for their contribution to the development of laser-based precision spectroscopy, including the optical frequency comb technique” (2005)
Gérard Mourou and Donna Strickland
“for their method of generating high-intensity, ultra-short optical pulses” 2018
Ahmed H. Zewail ”for his studies of the transition states of chemical reactions using femtosecond spectroscopy” 1999 (Chemistry)

## Slide 34
High Power Scaling: Heat is such a nuisance!
Increase surface-to-volume ratio (fibers, disks)

## Slide 35
Fiber Lasers

## Slide 36
Fiber Lasers
Single-Mode Fiber
6 µm core / 125 µm cladding
High Beam Quality
Lower Power Pumping
Expensive Pumping
Multimode Fiber
50 µm core / 125 µm cladding
Higher Power Pumping
Inexpensive Pumping
Poor Beam Quality
Optical Fiber Modes
Graphics: courtesy of Colin Diehl & Jered Richter

## Slide 37
Example: Erbium-Doped fiber Lasers
The wavelength of about 1550 nm is particularly interesting for applications in telecommunication.
EDFA: Erbium Doped Fiber Amplifier

## Slide 38
Fiber-optic Communications
wavelength (m)
1.5
1.0
attenuation coefficient (db/km)
1
0.3
Rayleigh
scattering
infrared
absorption
silica-glass fibers

## Slide 39
Fiber transmission line
signal
processing
transmitter
signal
processing
receiver
amplifier/
repeater
input
signal
6000 km
transatlantic US - UK
80000 simultaneous voice channels
repeaters 100 km apart
InGaAsP
diode laser

## Slide 40
Mainly: Yb Silica Fiber Lasers
Diode Pumped at 940-980 nm
Laser: 1020-1050 nm
High Power Fiber Lasers

## Slide 41
Double-Clad Fiber
Laser light propagates in single-mode core
Pump light propagates in inner cladding
High Power Fiber Lasers

## Slide 42
100 kW (current record)!

## Slide 45
D
d
Output-Coupler
Pump-Beam
Thin Disk Lasers
Yb:YAG
>10 kW CW
Requires multipass pumping

## Slide 46
Chemical Lasers
F + D2  DF* + D DF 3.5 - 4.1 m
Cl + HI  HCl* + I HCl 3.5 - 4.1 m
H +Br2  HBr* + Br HBr 4.0 - 4.7 m
F + H2  HF* + H HF 3.5 - 4.1 m
- population inversion is produced by a chemical reaction
A + BC AB + C*
- electrical power supply is not needed
- airborne lasers
- first chemical laser: 1964
Examples:
chemical reaction:
- exothermic
- generation rate must be large
enough to overcome spontaneous
emission and collisional relaxation
reaction active medium wavelength
I + O2*  I* + O2 I 1.31 m
molecules in an excited
vibrational state
atoms in an excited
electronic state

## Slide 47
The chemical oxygen-iodine laser (COIL): MW CW Power !!
chemical reaction:
O2(1 ) + I  O2(3 ) + I*
O2(1 )
I
energy transfer
O  I
O2(3 )
I*
1. generation of singlet oxygen Cl2 + H2O2 +2NaOH  O2(1 ) + 2H2O + 2NaCl
2. production of excited iodine O2(1 ) + I  O2(3 ) + I*
3. lasing of excited iodine
steps:
Singlet oxygen (dioxidene) has a >40 min lifetime.

## Slide 48
schematic diagram of a chemical iodine laser
parameters
MW ouput power
wavelength 1.315 micron
pulsed and cw
atmospheric absorption
singlet oxygen
iodine
mixer
supersonic
nozzle
laser
output
expanding
gas (cooling)
1
2
3
4
5
0.0
0.2
0.4
0.6
0.8
1.0
1 km propagation in atmosphere
absorption
wavelength (
m
m)
wavelength (mm)
absorption

## Slide 49
Free Electron Laser (FEL)
wiggler period
wiggler strength
(often <1)

## Slide 50
Semiconductor Lasers

## Slide 51: Laser Market and Applications

## Slide 52
What is a semiconductor?

## Slide 53
Direct-Gap vs. Indirect-Gap
E(energy)
k (momentum)

## Slide 55
Optical Interactions in a Direct-Gap Semiconductor

## Slide 56
A Brief Introduction to Semiconductors
Energy Bands
Equilibrium
E
1 0
Fermi-Dirac Statistics
http://britneyspears.ac/lasers.htm !!!???

## Slide 57
Nonequilibrium Electron-Hole Injection
104 cm-1
0
E
g
Absorption or
Gain
0
E
g
Absorption or
Gain
hw
Example
GaAs
Eg=1.4 eV
(g=850 nm)

## Slide 58
p-n junctions
Doping with Impurities
n-type
p-type
Eg
Ef
Eg
Ef
Examples: GaAs doped with Br
Si doped with P
Examples: GaAs doped with Zn
Si doped with Al
Section 12.1 p.2

## Slide 59
+ V
Inversion (Gain) Layer
Forward-Biased p-n Junction (LED)
n+-GaAs
p+-GaAs
d
Current Density Threshold
Recombination time
Semiconductor junction lasers

## Slide 60
Edge-Emitting Homojunction Laser Diodes
Waveguide Modes
Lg100 m
Homojunction Lasers have very high current threshold mainly because.
Electrons and holes are free to diffuse and therefore dilute the gain (no carrier confinement)
Optical mode has poor overlap with gain (no optical confinement or guiding)
Section 12.2 p.2

## Slide 61
12.3 Heterojunction Lasers Diodes
holes
GaAs
p+
AlGaAs
n+
AlGaAs
Energy
electrons
Index of Refraction
n when Eg
Carrier confinement
Mode confinement
A fortunate coincidence:
100 nm
holes

## Slide 62
Edge-Emitting Heterojunction Laser Diodes
Section 12.3 p.2
Edge-Emitting Buried Heterojunction Laser Diodes

## Slide 64
12.4 Quantum Well Lasers
p+
AlGaAs
n+
AlGaAs
10 nm
Multiple Quantum Well (MQW) Lasers
Epitaxial Growth
mode confinement

## Slide 65
High Power Diode Bars
P>100 W (cw)
Diode-pumping solid-state lasers (DPSS)
Material Processing
…
Section 12.4 p.2

## Slide 66
Vertical Cavity Surface Emitting Lasers (VCSEL)
Good mode quality couples to fiber efficiently for telecom applications
Single mode operation
2-D structures cam be made
Low power
Section 12.4 p.3

## Slide 67
Optically-Pumped Semiconductor Lasers (OPSL)

## Slide 68
Laser Diodes Cover the Spectrum
AlxGa1-xN GaN InxGa1-xN | uv uv (350 nm) blue (480-400 nm) | data storage, display
GaxI1-xP (x=0.5) GaxAl1-xAs (x=0-0.45) | 670 nm 620-895 nm | display
GaAs InxGa1-xAs (x=0.2) | 904 nm 980 nm | diode pumping solid-state and fiber lasers.
InxGa1-xAsyP1-y (x=0.73, y=0.58) (x=0.58, y=0.9) | 1100-1650 1310 nm 1550 nm | Telecom
PbSSe | 4200-8000 nm | cryogenic
PbSnTe | 6300-29,000 nm | cryogenic
Section 12.4 p.4
Compound | Spectral Region | Notes

## Slide 69
12.5 Recent Advances: Quantum Cascade Lasers

## Slide 70
Section 12.5 p.2

## Slide 71
THE END !